## Slide 1
ML-Guided Cut Selection for
ASIC Technology Mapping in ABC
Submitted By
Hemang Gautam
EDA Course Project • April 2026

## Slide 2
Problem Statement
• In ASIC technology mapping, the ABC tool generates structural "cuts" in an And-Inverter Graph (AIG) and selects the best ones to minimize area and delay.
• ABC uses greedy heuristics like Area Flow and MFFC to evaluate cuts, but these are local — they can miss globally optimal solutions.
• Increasing the cut limit (e.g., from C=8 to C=16) improves Quality of Results (QoR), but nearly doubles the CPU runtime.
• Goal: Can a machine learning model intelligently select superior cuts from the default pool (C=8), achieving the QoR of a larger pool without the runtime penalty?

## Slide 3
Motivation: Mapping Time vs. Cut Capacity
• We measured baseline CPU mapping time across 8 benchmarks while varying the max-cuts parameter (-C).
• As the cut limit increases, the runtime grows significantly while QoR gains diminish.
• This demonstrates the need for smarter cut selection rather than brute-force enumeration.
Max Cuts (-C) | Total CPU Time (s) | Normalized Time
2 | 1.225 | 0.37×
4 | 1.855 | 0.55×
6 | 2.489 | 0.74×
8 (default) | 3.352 | 1.00× (baseline)
12 | 4.666 | 1.39×
16 | 6.066 | 1.81×

## Slide 4
Our Approach: Overview
• We trained a lightweight Multi-Layer Perceptron (MLP) to score cuts based on 9 hand-engineered structural features.
• The trained model was converted into pure C code and integrated directly into ABC's mapping loop — no Python or file I/O at runtime.
• Instead of filtering cuts, we use an "Area Blending" strategy: the ML score gently adjusts ABC's internal area estimate during its area-recovery rounds.
• A conservative blending factor (α = 0.02) ensures the ML acts as an intelligent tie-breaker without disrupting ABC's convergence guarantees.
• This approach allows the ML signal to organically propagate through the mapping graph.

## Slide 5
Comparison with SLAP Framework
• SLAP (Supervised Learning for ASIC Performance) is a recent ML-for-mapping framework. Our approach diverges in two key ways:
• 1. Model Architecture
  ◦ SLAP uses complex Graph Neural Networks (GNNs) and PairNet structures to capture global circuit topology.
  ◦ We use a simple 3-layer MLP and compensate with carefully hand-crafted structural features (e.g., mffc_size, slack_ratio) computed natively by ABC.
• 2. Integration Strategy
  ◦ SLAP pre-filters cuts — scoring thousands and discarding weak ones before the mapper runs.
  ◦ We blend the ML score inline during ABC's dynamic programming phase, adjusting the area estimate in real time.

## Slide 6
ML Model: Architecture
• The model is a 3-layer feed-forward neural network, implemented in PyTorch and later exported to C.
  ◦ Input Layer: 9 neurons — one per structural feature
  ◦ Hidden Layer 1: 64 neurons with ReLU activation and 20% Dropout
  ◦ Hidden Layer 2: 32 neurons with ReLU activation and 20% Dropout
  ◦ Output Layer: 1 neuron producing a raw scalar quality score
• The model was trained on Google Colab using a T4 GPU.
• After training, the PyTorch weights were exported into a static C header file (model_weights.h) for native execution inside ABC.

## Slide 7
Feature Engineering
• A major challenge was avoiding label leakage. If the model is trained on ABC's own heuristic values (Area Flow, Delay), it simply learns to copy ABC and provides zero improvement.
• We selected 9 structural/topological features that ABC does not directly optimize:
  ◦ n_leaves, node_level, node_fanout — basic cut and node topology
  ◦ is_critical, slack_ratio — timing pressure indicators
  ◦ fanout_adj_area, area_per_leaf — structural interaction ratios
  ◦ mffc_size, mffc_per_leaf — Maximum Fanout-Free Cone efficiency
• cut_delay, area_flow, and required_time were used exclusively for constructing the training label and were never passed as input features.

## Slide 8
Label Formulation & Training Strategy
• Initial Attempt: Labels based on MFFC size alone. Result — exactly 0% QoR improvement because the model simply cloned ABC's existing heuristic.
• Final Label: We formulated labels based on the Area-Delay Product (ADP):
  ◦ Quality Score = −(Area Flow × Cut Delay)
  ◦ A higher quality score means a cut achieves lower area and delay simultaneously.
• We used a Pairwise MarginRankingLoss (RankNet approach). The model is shown pairs of cuts for the same node and is penalized if it incorrectly ranks the worse-ADP cut higher.
• Features are standardized using a fitted StandardScaler before training.

## Slide 9
Integration: Area Blending Architecture
• Unlike SLAP's pre-filter approach, we inject the ML score directly into ABC's area-recovery mapping rounds (Mode 2).
• The blending formula modifies ABC's internal area estimate:
Area_adjusted = Area_ABC × (1 − α · tanh(ML_Score))
• We used α = 0.02 — a conservative value that ensures the ML acts as a gentle tie-breaker for structurally similar cuts.
• The ML signal propagates organically through ABC's dynamic programming graph rather than overriding decisions.
• The C inference engine (ifML.c) executes the MLP forward pass using standard floating-point arithmetic with zero external dependencies.

## Slide 10
End-to-End Implementation Pipeline
• Step 00–02: Set up dependencies, instrument ABC to dump structural features, and analyze the profiling data.
• Step 03–04: Patch the ABC source code and generate training data across all benchmarks.
• Step 05: Clean data, engineer 9 structural features, and train the MLP on Google Colab (T4 GPU) using RankNet pairwise loss.
• Step 06: Export the trained PyTorch weights into a static C header file (model_weights.h).
• Step 07: Inject the ML inference engine and weights into the ABC source tree and recompile.
• Step 08: Run the final QoR comparison between baseline ABC and ML-guided ABC on all benchmarks.

## Slide 11
Challenges Faced & Debugging
• Challenge 1: The "Trivial Cut" Crashing Bug
  ◦ The ML model was initially allowed to force ABC to choose its highest-scoring cut after mapping.
  ◦ The model assigned extremely high scores to trivial cuts (single-input identity cuts with near-zero delay and area).
  ◦ This fractured the mapping graph, causing massive LUT bloat and segmentation faults.
  ◦ Resolution: Filter out trivial cuts (n_leaves < 2) before ML scoring.
• Challenge 2: The "Zero Improvement" Phase
  ◦ Even after fixing crashes, the model yielded exactly 0% difference from baseline ABC.
  ◦ Root causes: Label leakage (training on MFFC) and overriding cuts after convergence broke timing.
  ◦ Resolution: Switched to ADP-based labels and inline Area Blending architecture.

## Slide 12
Results: QoR Comparison (Arithmetic Benchmarks)
• Comparison of baseline ABC (C=8) vs ML-Guided ABC on complex arithmetic circuits.
Benchmark | ABC LUTs | ML LUTs | LUT Imp % | ABC ADP | ML ADP | ADP Imp %
adder | 254 | 254 | 0.00 | 12,954 | 12,954 | 0.00
bar | 1,456 | 1,456 | 0.00 | 43,680 | 43,680 | 0.00
div | 22,030 | 19,942 | +9.48 | 19,033,920 | 17,229,888 | +9.48
hyp | 44,508 | 41,969 | +5.70 | 186,666,552 | 176,017,986 | +5.70
log2 | 8,010 | 7,778 | +2.90 | 616,770 | 598,906 | +2.90
max | 842 | 831 | +1.31 | 47,152 | 46,536 | +1.31
multiplier | 5,929 | 5,683 | +4.15 | 314,237 | 301,199 | +4.15
sin | 1,464 | 1,421 | +2.94 | 61,488 | 59,682 | +2.94
sqrt | 5,724 | 5,180 | +9.50 | 5,912,892 | 5,350,940 | +9.50
square | 3,997 | 3,502 | +12.38 | 199,850 | 175,100 | +12.38

## Slide 13
Results: QoR Comparison (Random Control Benchmarks)
• Comparison of baseline ABC (C=8) vs ML-Guided ABC on random control circuits.
Benchmark | ABC LUTs | ML LUTs | LUT Imp % | ABC ADP | ML ADP | ADP Imp %
cavlc | 359 | 359 | 0.00 | 2,513 | 2,513 | 0.00
ctrl | 57 | 57 | 0.00 | 456 | 456 | 0.00
dec | 304 | 304 | 0.00 | 608 | 608 | 0.00
i2c | 365 | 362 | +0.82 | 1,460 | 1,448 | +0.82
int2float | 123 | 123 | 0.00 | 861 | 861 | 0.00
mem_ctrl | 12,104 | 11,914 | +1.57 | 302,600 | 297,850 | +1.57
priority | 219 | 218 | +0.46 | 6,789 | 6,758 | +0.46
router | 105 | 105 | 0.00 | 1,575 | 1,575 | 0.00
voter | 2,826 | 2,785 | +1.45 | 48,042 | 47,345 | +1.45

## Slide 14
Results: Summary & Analysis
• The ML-guided mapper was evaluated across 19 AIGER benchmarks.
• Average ADP Reduction (arithmetic mean): 2.63%
• Zero instances of QoR degradation across all benchmarks.
• Best-performing benchmarks:
  ◦ square (multiplier): 12.38% ADP improvement — largest gain observed
  ◦ sqrt: 9.50% ADP improvement
  ◦ div (divider): 9.48% ADP improvement
  ◦ hyp (hyperbolic): 5.70% ADP improvement
• The model shows strongest gains on complex arithmetic circuits where ABC's local heuristics are most likely to miss globally optimal cut selections.

## Slide 15
Codebase Structure
• abc/ — The modified ABC synthesis tool with our ML integration hooks.
• benchmarks/ — AIGER benchmark circuits (arithmetic and random control suites).
• ml_cut_project/ — Main ML pipeline directory containing:
  ◦ ml/ — Trained model weights (cut_model_mlp.pt) and feature scaler (scaler.pkl).
  ◦ abc_patch/ — Source patches: ifML.c (inference engine) and model_weights.h.
  ◦ data/ and results/ — Raw CSV dumps and QoR comparison logs.
• Core ABC Modifications:
  ◦ ifML.c — Contains the If_MLBlendCutArea function that runs the MLP forward pass.
  ◦ ifMap.c — Modified to call the ML blending function during area-recovery rounds.
  ◦ if.h — Updated header with forward declarations for the ML integration.

## Slide 16
Key Takeaways
• A lightweight MLP can outperform ABC's highly optimized, hand-tuned EDA heuristics when guided by the right features and labels.
• Avoiding label leakage is critical — training on structural features forces the model to learn genuinely new signals rather than copying ABC.
• Area Blending is superior to hard filtering because it preserves the optimizer's mathematical convergence guarantees.
• Native C integration (model_weights.h + ifML.c) eliminates all I/O overhead, making ML inference practical inside tight mapping loops.
• The results demonstrate that ML can act not just as an external filter, but as an embedded mathematical guide for traditional EDA algorithms.

## Slide 17
Conclusion
• This project successfully implemented an ML-guided ASIC technology mapper by deeply integrating a structural-feature-based MLP directly into ABC's C codebase.
• We overcame significant integration hurdles — trivial cut crashes, label leakage, and broken timing graphs — through systematic debugging.
• The Area Blending architecture proved to be the correct design choice, allowing ML to gently steer ABC's decisions.
• The final model achieved up to 12.38% ADP reduction on complex arithmetic circuits, with an average improvement of 2.63% and zero regressions.
• These results highlight the practical potential of machine learning for improving EDA tool quality without sacrificing runtime or stability.

## Slide 18
Thank You
Questions & Discussion